## Slide 1: BIO 201 Lab 1 Experiments 1, 2, 3
Professor Diane Hilker

## Slide 2: Overview
Exp. 1: Introduction to the Microscope
Exp. 2: Survey of Microbes
Exp. 3: Collection of Microbes

## Slide 3: I. Exp. 1: Intro. to the Microscope
Purpose: To review
the use & care of the
compound light
microscope
Fig. 3.1 Textbook

## Slide 4: I. Exp. 1: Intro. to the Microscope
Compound Binocular Light Microscope
  (2) Sources of Magnification:
    Eyepiece or Ocular (10x)
    Objectives (4):
      Scanning Power: 4 x
      Low Power: 10x
      High Power: 40x
      Oil Immersion: 100x
Parfocal: ability to go from one objective to another with minimal focusing

## Slide 5: I. Exp. 1: Intro. to the Microscope
Total Magnification: TM
  TM=Magnification of Eyepiece X
  Magnification of Objective
 | Eyepiece Magnification | Objective Magnification | TM
Scanning | 10X | 4X | 40X
Low | 10X | 10X | 100X
High Dry | 10X | 40X | 400X
Oil Immersion | 10X | 100X | 1000X

## Slide 6: I. Exp. 1: Intro. to the Microscope
Resolution or Resolving Power (RP)
  Ability to distinguish detail clearly
  To be able to tell 2 points as separate points and not one point
  RP = Wavelength of Light = -------
2 X Numerical Aperture 2NA

## Slide 7: I. Exp. 1: Intro. to the Microscope
Wavelength of light (nm)
Red light = 700 nm
Blue light = 400 nm
RP red = 700 nm = 350 nm
2(1)
RP blue = 400 nm = 200 nm
2(1)
Lower the resolution, better the clarity
Blue filter provides the best resolution with a halogen light bulb
Blue filter NOT needed with microscopes that have
a LED light bulb

## Slide 8: I. Exp. 1: Intro. to the Microscope
Numerical Aperture (NA): describes the cone of light that enters the lens so as to see fine detail. Two things make up NA:
  Angular Aperture: angle of light as it goes through the lenses & filters of the condenser & into the objective (Constant)
  Refractive Index: how light travels through a medium
    Refractive Index of Air = 1.0
    Refractive Index of Oil = 1.5

## Slide 9: I. Exp. 1: Intro. to the Microscope
RP air= 400 nm = 200 nm
2(1.0)
RPoil = 400 nm = 133 nm
2(1.5)
Better resolution
with oil

## Slide 10: Overview
Exp. 1: Introduction to the Microscope
Exp. 2: Survey of Microbes
Exp. 3: Collection of Microbes

## Slide 11: II. Exp. 2: Survey of Microbes
Purpose: To become familiar with using a microscope & to view various microbes
  Wet Mount: observing living cells
    Focus on edge of coverslip
    Scanning-dim light using diaphragm
    Move toward center of slide
    Observe under Low & High
    Powers
    Slides will dry out quickly

## Slide 12: II. Exp. 2: Survey of Microbes
4 Slides: Largest to smallest microorganisms
1. Pond Water: algae-much variation

## Slide 13: II. Exp. 2: Survey of Microbes
2. Protozoa: single celled eukaryotic microbes
that move by different methods that belong to
the Protista kingdom.
  Pseudopods: false feet
  Amoeba
  Cilia
  Paramecium
  Flagella
  Euglena

## Slide 14: II. Exp. 2: Survey of Microbes
3. Yeast: single celled eukaryotic microbes
that belong to the Fungi kingdom
    Ovoid & irregular
    Budding: method of
    reproduction
    Brownian movement
    Smaller than protozoa
    Larger than bacteria

## Slide 15: II. Exp. 2: Survey of Microbes
4. Bacteria (Hay infusion ): single celled prokaryotic microbes that belong to the Eubacteria Domain.
    Must view under 400x
    Very small
    Motile & non-motile
    Looks like specks of sand
    Hard to discern shape
    Smaller than yeast
    & protozoa
    Protozoa may be present in the sample

## Slide 16: Overview
Exp. 1: Introduction to the Microscope
Exp. 2: Survey of Microbes
Exp. 3: Collection of Microbes

## Slide 17: III. Exp. 3: Collection of Microbes
Purpose: To collect and grow microbes from the environment for observation
  Procedure to be described by lab instructor