## Slide 2: Technology in Action
Chapter 9
Behind the Scenes: A Closer Look at System Hardware
Notes: This chapter builds on what you’ve learned about computer hardware in other chapters and goes behind the scenes, looking at your system unit’s components in more detail. First we examine how computers translate the commands you input into the digits they can understand: 1s and 0s. Next, we analyze the internal workings of the CPU and memory. We then look at buses, the highways that transport data between the CPU, memory, and other devices connected to the computer.

## Slide 3: Chapter Topics
Computer switches
Binary number system
Inside the CPU
Cache memory
Types of RAM
Computer buses
Creating faster CPUs
Notes: Chapter topics include:
Computer switches
Binary number system
Inside the CPU
Cache memory
Types of RAM
Computer buses
Creating faster CPUs

## Slide 4: Binary Language
Computers work in binary language
Consists of two numbers: 0 and 1
Everything a computer does is broken down into a series of 0s and 1s
Switches: Devices inside the computer that can be flipped between these two states: 1 or 0, on or off
Notes: To process data into information, computers need to work in binary language, which consists of two numbers: 0 and 1.
Everything a computer does is broken down into a series of 0s and 1s.
Because modern computers are electronic, digital machines, they understand only two states of existence: on and off. Computers represent these two possibilities, or states, using the digits1 and 0.
Electronic switches are devices inside the computer that can be flipped between these two states: 1 or 0, on or off.

## Slide 5: Switches
Nonmechanical devices in computers that open and close circuits
Types of electrical switches:
  Vacuum tubes
  Transistors:
    Semiconductors
  Integrated circuits
Vacuum Tube
Transistors
Integrated Circuits
Notes: Early computers used devices called vacuum tubes as switches. Vacuum tubes act as computer switches by allowing or blocking the flow of electrical current. The problem with vacuum tubes is that they take up a lot of space and they produce a lot of heat. Thus, vacuum tubes make for impractical switching devices in personal computers.
Since the vacuum tubes, two major revolutions have occurred in the design of switches, and consequently computers, to make them smaller and faster: the invention of the transistor and the fabrication of integrated circuits.
Transistors are electrical switches built out of layers of a special type of material called a semiconductor. A semiconductor is any material that can be controlled to either conduct electricity or act as an insulator. Silicon, which is found in common sand, is the semiconductor material used to make transistors.
Integrated circuits (or chips) are very small regions of semiconductor material that support a huge number of transistors. Along with all the many transistors, other components critical to a circuit board (such as resistors, capacitors, and diodes) are also located on the integrated circuit. Most integrated circuits are no more than a quarter inch in size.
Integrated circuits have enabled computer designers to create small yet powerful microprocessors, which are chips that contain a CPU.

## Slide 6: Switches Representing Data
The on/off state of a switch represents one bit of data
Bit (binary digit)
  On = 1
  Off = 0
OFF
0
ON
1
0
1
OR
= 1 bit
Notes: To manipulate the on/off switches, the computer works in binary language, which uses only two digits, 1 and 0.
On is 1 and off is 0. Thus, electricity becomes numbers.

## Slide 7: The Binary Number System
Describes a number as powers of 2
Also referred to as base 2 numbering system
Used to represent every piece of data stored in a computer: all of the numbers, letters, and instructions
Notes: Computers describe a number as powers of 2 because each switch can be in one of two positions: on or off. This numbering system is referred to as the binary number system. It is the number system used by computers to represent all data.
Because it only includes two digits, the binary number system is also referred to as the base 2 number system.
Binary numbers are used to represent every piece of data stored in a computer: all of the numbers, all of the letters, and all of the instructions that the computer uses to execute work.

## Slide 8: The Binary Number System
Number systems are organized ways to represent numbers
Each number in one system has a corresponding number in another.
01011001 = 89
Binary Base 10
 | 128 2x64 | 64 2x32 | 32 2x16 | 16 2x8 | 8 2x4 | 4 2x2 | 2 2x1 | 1 | 
Binary | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 
Base 10 | 0 + | 64 + | 0 + | 16 + | 8 + | 0 + | 0 + | 1 = | 89
Notes: In the base 10 number system, a whole number is represented as the sum of ones, tens, hundreds, and thousands—sums of powers of 10. The binary system works in the same way but describes a value as the sum of groups of 64s, 32s, 16s, 8s, 4s, 2s, and 1s—that is, powers of 2: 1, 2, 4, 8, 16, 32, 64, and so on.

## Slide 9: Representing Letters and Symbols
American Standard Code for Information Interchange (ASCII)
  8 bits = 1 byte = alphanumeric character or symbol
  256 different combinations
Unicode
  16 bits equal 1 byte
  65,000 different combinations, used for all languages
Notes: To provide a consistent means for representing letters and other characters, there are codes that dictate how to represent characters in binary format. Most of today’s computers use the ASCII code to represent each letter or character as an 8-bit binary code.
The ASCII code represents the 26 uppercase letters and 26 lowercase letters used in the English language, along with a number of punctuation symbols and other special characters, using 8 bits.
The ASCII code can assign only 256 (or 28) different codes for unique characters and letters. Although this is enough to represent English and many other characters found in the world’s languages, ASCII code cannot represent all languages and symbols.
Thus, a new encoding scheme, called Unicode, was created. By using 16 bits instead of the 8 bits used in ASCII, Unicode can represent more than 65,000 unique character symbols, enabling it to represent the alphabets of all modern languages and all historic languages and notational systems.

## Slide 10: ASCII Chart
Notes: ASCII stands for the American Standard Code for Information Interchange. It serves as the foundation for electricity becoming information.

## Slide 11: The CPU: Processing Digital Information
The CPU is the brains of the computer
Different types of CPUs
  Intel and AMD chips: Used in most Windows-based PCs
  Apple systems use different CPU design
Differentiating CPUs
  Processing power
  Clock speed and cache
Notes: The central processing unit (CPU or processor) executes every instruction given to your computer. The entire CPU fits on a tiny chip, called the microprocessor, which contains all of the hardware responsible for processing information, including millions of transistors.
The CPU is located in the system unit on the computer’s motherboard.
Both Intel and AMD chips are used in the majority of Windows-based PCs. Apple computer systems use a different CPU design. The G4 and PowerPC G5 chip were used by Apple machines for over 10 years. In 2005, Apple announced that all of their systems would be redesigned to use Intel CPUs.
The primary distinction between CPUs is processing power, which is determined by the number of transistors on each CPU. The greatest differentiators are how quickly the processor can work (called its clock speed) and the amount of immediate access memory the CPU has (called its cache memory).

## Slide 12: Processors on the Market

## Slide 13: The CPU Machine Cycle
Fetch
  The program’s binary code is “fetched” from its temporary location in RAM and moved to the CPU
Decode
  The program’s binary code is decoded into commands that the CPU understands
Execute
  The ALU performs the calculations
Store
  The results are stored in the registers
Notes: Any program you run on your computer is actually a long series of binary code, 1s and 0s, describing a specific set of commands the CPU must perform. Each CPU is a bit different in the exact steps it follows to perform its tasks, but all CPUs must perform a series of similar general steps. These steps, referred to as a CPU machine cycle (or processing cycle), are:
1. Fetch: When any program begins to run, the 1s and 0s that make up the program’s binary code must be “fetched” from their temporary storage location in RAM and moved to the CPU before they can be executed.
2. Decode: Once the program’s binary code is in the CPU, it is decoded into the commands the CPU understands.
3 Execute: Next, the CPU actually performs the work described in the command. Specialized hardware on the CPU performs addition, subtraction, multiplication, division, and other mathematical and logical operations at incredible speeds.
4. Store: The result is stored in registers, special memory storage areas built into the CPU, which are the most expensive, fastest memory in your computer. The CPU is then ready to fetch the next set of bits encoding the next instruction.

## Slide 14: The System Clock
Located on the motherboard
Controls the CPU’s processing cycles
Clock cycle
  Pulse or tick
Clock speed
  Number of pulses per second
  Measured in hertz (Hz)
Notes: To move from one stage of the machine cycle to the next, the motherboard contains a built-in system clock.
This internal clock is a special crystal that controls when the CPU moves to the next stage of processing.
These “ticks” of the system clock, known as the clock cycle, set the pace by which the computer moves from process to process.
The pace, known as clock speed, is measured in Hz. Today’s system clocks are measured in GHz, or one billion clock ticks per second.

## Slide 15: The Control Unit
Manages the switches inside the CPU
Is programmed by CPU designers to remember the sequence of processing stages for that CPU
Moves each switch to its correct setting (on or off)
Then performs the work of that stage
Notes: The control unit of the CPU manages the switches inside the CPU.
It is programmed by CPU designers to remember the sequence of processing stages for that CPU and how each switch in the CPU should be set, on or off, for each stage.
As soon as the system clock says so, the control unit moves each switch to its correct setting (on or off) and then performs the work of that stage

## Slide 16: The Arithmetic Logic Unit (ALU)
Part of the CPU designed to perform mathematical operations (addition, subtraction, multiplication, division, etc.)
Also performs logical OR, AND, and NOT operations
Is fed data from the CPU registers
  Word size: Number of bits a computer can work with at a time
Notes: The arithmetic logic unit (ALU) is the part of the CPU designed to perform mathematical operations such as addition, subtraction, multiplication, and division and to test comparing values as greater than, less than, or equal to.
The ALU also performs logical OR, AND, and NOT operations. The ALU is specially designed to execute such calculations flawlessly and with incredible speed.
The ALU is fed data from the CPU’s registers. The amount of data a CPU can process at a time is based in part on the amount of data each register can hold. The number of bits a computer can work with at a time is referred to as its word size. Therefore, a 64-bit processor can process more information faster than a 32-bit processor.

## Slide 17: Cache Memory
Small amount of memory located on the CPU chip or near it
Stores recent or frequently used instructions and data
Used for quick access by the CPU
Different levels of cache
Notes: Cache memory consists of small blocks of memory located directly on and next to the CPU chip.
These memory blocks are holding places for recently or frequently used instructions or data that the CPU needs the most.
When these instructions or data are stored in cache memory, the CPU can more quickly retrieve them than if it had to access the instructions or data in RAM.
Modern CPU designs include a number of types of cache memory. Level 1 cache is a block of memory that is built onto the CPU chip for the storage of data or commands that have just been used. Level 2 cache is located on the CPU chip, but is slightly farther away from the CPU, or it’s on a separate chip next to the CPU and therefore takes somewhat longer to access. Some newer CPUs have an additional third level of cache memory storage, called Level 3 cache.

## Slide 18: RAM: The Next Level of Temporary Storage
Volatile: When you turn off your computer, the data is erased
Several kinds of RAM exist
Each type of RAM has a different design
  Some types work at much faster speeds
  Some transfer data more quickly
Notes: Random access memory (RAM) is volatile, meaning that when you turn off your computer, the data stored in RAM is erased.
There are several kinds of RAM. Each type of RAM has a very different internal design, allowing some types to work at much faster speeds and to transfer data much more quickly than others.

## Slide 19: Types of RAM: DRAM
Cheapest and most basic type of RAM
Loses its electrical charge, needs to be refreshed
Many types of DRAM
  SDRAM: Synchronous DRAM
  DDR SDRAM: Double data rate SDRAM
Notes: The cheapest and most basic type of RAM is dynamic RAM (DRAM). It is used in older systems or in systems in which cost is an important factor.
In storing 1 bit of data inside DRAM, a transistor and a capacitor are used. A transistor is a switch that can be turned on or off. A capacitor is a device that acts like a storage space for the charged electrons coming from the transistors. To store a 1, the transistor is turned to the “on” position and it fills the capacitor with charge.
If the capacitor is just filled with charge once, it eventually loses its charge. A 1 bit might now be read as a 0 and the data stored there would be corrupted. To make sure each capacitor holding a 1 value is filled with enough charge to be read as a 1 at any time, a refresh signal is applied. The refresh will flood current through the open transistors to refill the capacitors so they continue to store a valid 1.
A variety of types of DRAM are on the market, each with different performance levels and prices.
-Synchronous DRAM (SDRAM) is much faster than traditional DRAM.
-The current standard of DRAM in home systems is double data rate synchronous DRAM (DDR SDRAM). DDR SDRAM is faster than regular SDRAM but not as fast as DDR2 SDRAM, which is the most recent entry on the market.
Each of these types of DRAM increases the speed with which the CPU can access data, but also increases the cost of the memory modules.

## Slide 20: Types of RAM: SRAM
Static RAM (SRAM)
  Does not lose its electrical charge
  Faster than DRAM
  More expensive than DRAM
  Used only in locations like cache memory
Notes: All of the refresh signals required to keep the data “fresh” in DRAM take time. A faster type of RAM is static RAM (SRAM).
In SRAM, more transistors are used to store a single bit, but no capacitor is needed. This eliminates the need for a refresh signal, thus making SRAM much faster than DRAM.
However, because it is more expensive than DRAM, it is used only in locations such as the CPU’s cache, where the system demands the fastest possible storage.

## Slide 21: Buses: The CPU’s Data Highway
Bus
  Electrical pathway used to move data between components
  Local bus or front side bus (FSB): Connects the CPU with the memory
  Expansion bus: Connects the CPU with peripheral devices
01100010
01110011
01001000
00100111
Notes: A bus is an electrical wire in the computer’s circuitry—the highway that data (or bits) travels on between the computer’s various components.
Computers have two different kinds of buses.
-Local buses (or front side buses) are on the motherboard and run between the CPU and the main system memory.
- Most systems also have another type of bus, called an expansion bus, which expands the capabilities of your computer by allowing a range of different expansion cards (such as video cards and sound cards) to communicate with the motherboard.

## Slide 22: Bus Performance
Bus clock speed
  Rate of speed data moves from one location to another
  Measured in MHz (millions of clock cycles per second)
Bus width
  The number of bits of data moved on a bus at any one time
  Measured in bits
    16 bits
    32 bits
Notes: Some buses move data along more quickly than others, whereas some can move more data at one time.
The rate of speed that data moves from one location to another, known as bus clock speed, affects the overall performance of the computer. Bus clock speed is measured in units of megahertz (MHz), or millions of clock cycles per second. Systems on the market now have FSB speeds ranging from 667 MHz to 1066 MHz
The width of the bus (or the bus width) determines how many bits of data can be sent along a given bus at any one time. The wider the bus, the more data that can be sent at one time. Bus width is measured in terms of bits, so a 32-bit bus can carry more data at one time than a 16-bit bus.

## Slide 23: Types of Expansion Buses
ISA and EISA
  Found on older computers
  Connect mouse, modem, and sound card
PCI
  Faster than ISA and EISA
  Found on modern computers
  Connects network, modem, and sound cards
AGP
  Used for three-dimensional graphics
  Connects the graphics card and memory
Notes: Expansion buses provide the pathways that enable the CPU to communicate with the peripheral devices attached through expansion cards.
Expansion buses have evolved to provide faster transfer speeds and wider bit widths to deliver higher data transfer rates to the many peripheral devices you may connect to your computer.
There are several types of expansion buses.
-Older computers include buses such as the Industry Standard Architecture (ISA) bus and the Extended Industry Standard Architecture (EISA) bus to connect devices such as the mouse, modem, and sound cards. These are being replaced by faster, more efficient connections.
-In a modern computer system, you’ll find Peripheral Component Interconnect (PCI) buses. PCI expansion buses connect directly to the CPU and support such devices as network cards and sound cards.
-On current systems, you’ll also find Accelerated Graphics Port (AGP) buses. The AGP bus design was specialized to help move three-dimensional graphics data quickly. It establishes a direct pathway between the graphics card and main memory so that data does not have to ride on the PCI bus, clogging up other system data being moved about.

## Slide 24: Making Computers Faster
Pipelining: The CPU processes more than one instruction at a time
Fetch
Decode
Execute
Store
Fetch
Decode
Execute
Store
Instruction 1
Instruction 2
Nonpipelined CPU
Fetch
Decode
Execute
Store
Fetch
Decode
Execute
Store
Fetch
Decode
Execute
Store
Fetch
Decode
Execute
Store
Instruction 1
Instruction 2
Instruction 3
Instruction 4
Pipelined CPU
Notes: One method found to speed up a CPU is called pipelining.
As an instruction is processed, the CPU runs through the four stages of processing in a sequential order: fetch, decode, execute, store. Pipelining is a technique that allows the CPU to work on more than one instruction (or stage of processing) at a time, thereby boosting CPU performance. and is used in some fashion in all modern CPUs.
Instead of the CPU carrying out one step of the machine cycle on every pulse of the system clock, the CPU performs different parts of the cycle simultaneously, theoretically making the CPU four times faster. Chip makers have also designed special instruction sets to handle multimedia content, again speeding up the overall performance of the system.

## Slide 25: Making Computers Faster
Specialized instructions for handling
  Multimedia
  Graphics
Notes: Each design team developing a new CPU tries to imagine what users’ greatest needs will be in four or five years. Currently, several processors on the market reflect this consideration in the incorporation of specialized multimedia instructions into the basic instruction set. T
he hardware engineers have redesigned the chip so that the instruction set contains new commands that are specially designed to speed up the work needed for video and audio processing.

## Slide 26: Making Computers Faster
Dual processing
  Two CPUs on the same system
  Each processor shares the workload
Multi-core processing
Hyperthreading
Parallel processing
  Network of computers
  Each computer works on a portion of the problem simultaneously
Notes: Many high-end server systems employ dual processors, two completely separate CPU chips on one motherboard.
Intel is promoting a technology called multi-core processing in its Core 2 Duo line of chips. Chips with multi-core processing capabilities have two separate parallel processing paths inside them, so they are almost as fast as two separate CPUs.
Hyperthreading technology allows the CPU to run four tasks (fetch, decode, execute, and store) at one time.
In parallel processing, there is a large network of computers, with each computer working on a portion of the same problem simultaneously.

## Slide 27: Chapter 9 Summary Questions
What is a switch and how does it work in a computer?
Notes: What is a switch and how does it work in a computer?

## Slide 28: Chapter 9 Summary Questions
What is the binary number system, and what role does it play in computer system?
Notes: What is the binary number system, and what role does it play in computer system?

## Slide 29: Chapter 9 Summary Questions
What is inside the CPU, and how do these components operate?
Notes: What is inside the CPU, and how do these components operate?

## Slide 30: Chapter 9 Summary Questions
How does a CPU process data and instructions?
Notes: How does a CPU process data and instructions?

## Slide 31: Chapter 9 Summary Questions
What is cache memory?
Notes: What is cache memory?

## Slide 32: Chapter 9 Summary Questions
What types of RAM are there?
Notes: What types of RAM are there?

## Slide 33: Chapter 9 Summary Questions
What is a bus, and how does it function in a computer system?
Notes: What is a bus, and how does it function in a computer system?

## Slide 34: Chapter 9 Summary Questions
How do manufacturers make CPUs so that they run faster?
Notes: How do manufacturers make CPUs so that they run faster?