## Slide 2: Technology in Action
Technology in Focus:
Digital Entertainment
Notes: In this Technology in Focus, we look at two popular forms of digital entertainment, digital photography and digital video, as well as what makes digital special.

## Slide 3: Analog vs. Digital Entertainment
Notes: Today, no matter what you’re interested in—music, movies, television, radio—a digital version is popular, as shown here.

## Slide 4: What’s Special About Digital?
Analog
  Sound and light waves
  Continuous waveforms
Digital
  Describes sound and light as a string of binary data representations (1s and 0s)
  Provides exact reproduction of sounds and color
Notes: Think about the information captured in music and film: sounds and images. Sound is carried to your ears by sound waves. Images are our interpretation of the changing intensity of light waves around us. These sound and light waves are called analog or continuous waves. They are continuous signals because you would never have to lift your pencil off the page to draw them: they are just one long continuous line.
Digital formats are descriptions of these signals as a long string of binary data representations (1s and 0s). This is the main reason why digital recording has such an advantage over analog. Digital gives us a simple way to describe sound and light waves exactly, so sounds and images can be reproduced perfectly each time.

## Slide 5: Analog-to-Digital Conversion
Notes: How could a digital format, a sequence of numbers, act as a convenient way to express these complicated wave shapes? The answer is provided by something called analog-to-digital conversion.
In analog-to-digital conversion, the incoming analog signal is measured many times each second. The strength of the signal at each measurement is recorded as a simple number. The series of numbers produced by the analog-to-digital conversion process gives us the digital form of the wave.
This figure shows how the process of creating digital entertainment begins with the physical act of playing music, which creates analog waves. Next, a chip inside the recording device called an analog-to-digital converter (ADC) digitizes these waves into a series of numbers. This series of numbers can be recorded onto CDs, DVDs, or sent electronically. On the receiving end, a playback device, such as a CD player or DVD player, is fed that series of numbers. Inside the playback device, a digital-to-analog converter (DAC), a chip that converts the digital numbers to a continuous wave, reproduces the original wave exactly.
How accurate it is, how close the digitized wave is in shape to the original analog wave, depends on the sampling rate of the ADC. The sampling rate specifies the number of times the analog wave is measured each second. The higher the sampling rate, the more accurately the original wave can be re-created.

## Slide 6: Digital Photography
Digital cameras: Capture and convert images to digital data
Notes: Digital cameras capture images on electronic sensors and then convert those images to digital data, a long series of numbers that represents the color and brightness of millions of points in the image.

## Slide 7: Digital Camera Selection
“Point and click” or single lens reflex (SLR)
Research cameras online
  Construction quality
  Features
  Image quality
  Ease of use
  Value for the cost
Notes: Single lens reflex cameras allow the user to switch between lenses and offer features that professional photographers need.
The website www.dpreview.com is a resource that evaluates digital cameras on their construction, features, image quality, ease of use and value for the cost.

## Slide 8: Digital Camera Resolution
Number of data points used in an image
Measured in megapixels
  Mega means millions
  Pixels are picture elements
Point-and-click camera resolution
  2 MB to 10 MB
SLR camera resolution
  Up to 16.7 MB
Notes: A pixel is a single dot in the make-up of a digital picture. Digital pictures are made up of millions of dots or pixels.
A point-and-click digital camera will have a resolution anywhere from 2MB to 10MB.
An SLR camera may have a resolution of up to 16.7 MB but are very expensive.

## Slide 9: Digital Camera Storage
Images are stored in a flash memory card
Notes: When a digital camera takes a photo, it stores the images on a flash memory card inside the camera.
Flash memory cards are very small and convenient, allowing you to easily transfer digital information between your camera and your computer or printer.

## Slide 10: Digital Photo File Formats
Notes: To fit more photos on the same size flash card, digital cameras allow you to choose from several different file types in order to compress the image data into less space.
When you choose to compress your images, you will lose some of the detail, but in return you’ll be able to fit more images on your flash card.
Here you see the most common file types supported by digital cameras: the RAW uncompressed data type and the Joint Photographic Experts Group (JPEG) type.
-RAW files record all of the original image information and so are larger than compressed JPEG files.
-JPEG files can be compressed just a bit, keeping most of the details, or compressed a great deal, losing some detail.

## Slide 11: Preparing to Take Photos
Take a spare battery pack
Be sure the flash card is installed
Set the resolution
Decide whether to use Autofocus
Check image stabilization
Immediately delete unwanted photos
Notes: Because digital cameras use batteries quickly a user should have a backup batter on hand.
Be sure the flash card is installed and that is has enough space on it for the number of pictures that are going to be taken.
Be sure to set the resolution. Consider if the photo will be enlarged. If you are going to enlarge the photo, use the highest resolution available on your camera.
Most digital cameras come with autofocus and they will automatically set the aperture and correct shutter speed.
Deleting unwanted photos immediately will free up space on the flash card.

## Slide 12: Transferring Photos to a Computer
Methods of transferring images
  USB ports
  Flash card readers
  Wireless
Notes: Transferring your photos to your computer is simple.
All current model digital cameras have a built-in USB 2.0 port. Using a USB 2.0 cable, you can connect the camera to your computer to store the converted images as uncompressed files or in a compressed format as JPEG files.
Another option is to transfer the flash card from your camera to the computer. Some desktops have flash card slots on the front of the system unit. However, if yours does not, you can buy an external memory card reader and attach it to your computer using an available USB port.
Many newer inkjet printers have a slot for reading a flash card. From here the pictures can be transferred to the computer or printed directly.
Several recent model cameras also support a wireless network connection.

## Slide 13: Making Old Photos Digital
Digital scanners
  Convert paper images into digital
  Some scan film negatives
  Quality is determined by resolution
    DPI (dots per inch)
  Connect via USB or Firewire
  Some support OCR
    Optical character recognition
Notes: Old photos or paper pictures can be converted into a digital format using a digital scanner.
Some of these scanners will accept file negatives or slides.
The resolution of a scanner refers to the number of pixels it uses to create a picture.
Resolutions up to 4,800 x 9,600 dpi are common on today’s scanners.
Scanners can be connected to your computer using USB 2.0 or FireWire ports
OCR software allows typed documents to be scanned in and placed in a file that can then be edited by using word processing software.

## Slide 14: Enhancing Photos and Adding Special Effects
Image-editing software
  Comes with camera
  More powerful programs: Adobe Photoshop, Corel Paint Shop Pro
Types of enhancement
  Remove red-eye
  Crop
  Correct color balance
  Add filtering effects
Dabble
Emboss
Ripple
Original
Click to see various photo effects
Notes: Once you’ve taken your photos, you may want to process them. With digital photography, you can do this using inexpensive image-editing software.
There are hundreds of image-editing programs available, from freeware to sophisticated suites. Many times the manufacturer of your camera will include an image-editing program with your camera. If you want to purchase a more powerful program, Adobe Photoshop and Corel Paint Shop Pro are two well-reviewed packages.
Software allows you to remove flaws such as red-eye; crop images; correct poor color balance; apply filtering effects such as mosaics, charcoal, and impressionistic style; and merge components from multiple images.

## Slide 15: Printing Photos
Photo printers
  Ink-jet
  Dye-sublimation
Ink-jet
Dye-sublimation
Notes: Once you’ve processed your photos, you can print them using a professional service or your own printer.
Photo printers for home use are available in two technologies: ink-jet and dye sublimation.
-Most popular and inexpensive are ink-jet printers, some of which are capable of printing high-quality color photos, although they vary in speed and quality.
-Dye-sublimation printers produce images using a heating element instead of an ink-jet nozzle. The heating element passes over a ribbon of translucent film that has been dyed with bands of colors. If you’re interested in a printer to use for printing only photographs, a dye-sublimation printer is a good choice. However, some models print only specific photo sizes, so be sure the printer you buy will fit your long-term needs.

## Slide 16: Digital Video
Cell phones
Digital cameras
Webcams
Digital video cameras
  Small and light weight
  Built-in hard disks
  DVD
  Transfer files using FireWire or USB 2.0
Older Model
Notes: Some cell phones and some digital cameras are capable of recording digital video.
Many digital video cameras save on to a built-in hard drive and some models even save directly onto DVD.
Transferring the video to a computer is simply a matter of plugging in the FireWire or USB 2.0 cable and following the software directions. The cameras can also play directly on a television using the video and audio out cables.

## Slide 17: Preparing to Shoot Video
Check battery power
Bring a backup battery
Check storage capacity
Use automated programs to control the exposure settings
Use the antishake feature
Notes: Be sure to check the battery’s power before shooting.
Consider bringing an extra charged battery.
Check your storage device to make sure you have enough storage for what you intend to shoot.
Automated programs control the exposure settings for different environments (nighttime shots, action events, and so on), while automatic focusing and telephoto zoom lens features are common as well.
The antishake feature stabilizes your image when not using a tripod with the camera.

## Slide 18: Transferring Video to the PC
Hardware
  USB 2.0
  DVD
  Flash memory
Software
  Windows Import Video
  Windows Movie Maker
  Adobe Premiere
  Pinnacle Studio DV
Notes: Some digital video cameras now offer a USB 2.0 port; you can then connect the camera to any free USB 2.0 port on your computer.
Some digital video cameras allow you to send your video directly to a DVD through your computer.
Some digital video cameras allow you to store video on flash memory cards. These cards can then be used to copy the video to your computer.
Once you connect your camera to your computer, Microsoft Windows Vista automatically identifies it, recognizing its manufacturer and model. The Windows OS then scans the software on your system and presents a list of all the programs you can use to import your video.
Windows Import Video is the default program for importing if you have no other software installed. Windows Movie Maker is another video-editing program. Other digital video-editing programs such as Adobe Premiere and Pinnacle Studio DV can import video as well.

## Slide 19: Editing Video and Adding Special Effects
Video-editing software
  Includes a storyboard
  Allows you to
    Review clips frame by frame
    Change sequence of frames
    Add transitions, titles, etc.
Notes: Video-editing software presents a storyboard or timeline with which you can manipulate your video file. Using this software, you can review your clips frame by frame or trim them at any point. You can order each segment on the timeline in whichever sequence you like and correct segments for color balance, brightness, or contrast.
In addition, you can add transitions to your video—fades to black, dissolves, and so on.
The website www.izzyvideo.com provides video podcasts to teach how to make the most impact with the editing and effects you apply to your raw video footage.

## Slide 20: Distributing Video
Notes: Once you’re done editing your video file, you can save (or export) it in a variety of formats. This chart shows some of the popular video file formats in use today, along with the file extensions they use.
Your choice of file format will depend on what you want to do with your video. For example, the RealMedia streaming file format is a great choice if your file is very large and you’ll be posting it on the Web. The Microsoft AVI format is a good choice if you’re sending your file to a wide range of users because it’s very popular and commonly accepted as the standard video format on Windows machines.

## Slide 21: New Options for Quick Video Delivery
Post videos on the web (www.youtube.com)
Use a “Flip” camcorder
Some cell phones record digital video
Webcams
Notes: A popular web site for posting videos is www.youtube.com
The Flip camcorder has built-in software that allows you to upload videos directly to www.youtube.com.
Some cell phones are capable of recording short digital videos.
Webcams allow you to send video to www.youtube.com with one click of a button.